## Slide 1
KURUKSHETRA 2.0 | 24-HR HACKATHON | FABTECH TECHNICAL CAMPUS, SANGOLA
AURA-X
AI-Powered Disaster Response Rover
Sees with AI. Thinks at the edge. Reports over LoRa.
Keeps responders in control.
AI & Intelligent Automation
IoT & Embedded Automation
Team: [Team Name] | Members: [Add names] | Domain: AI + IoT
Real-terrain prototype concept: 4WD chassis, ESP32-CAM, mmWave radar, LoRa

## Slide 2
01 THE PROBLEM
The first look inside a disaster is the most dangerous
Hazardous
Collapses, fires and floods put rescuers at risk before anyone knows what is inside.
Blind
Debris, smoke and darkness hide survivors from responders at the entrance.
Disconnected
Wi-Fi and cell networks fail exactly where help is needed most.
Collapsed buildings
Debris search
Night operation
Supply delivery
The need: a low-cost robot that goes in first, flags possible people and reports back.

## Slide 3
02 THE SOLUTION
AURA-X: a rugged AI rover that goes in first
DETECT
ESP32-CAM + vision AI flags possible people; mmWave radar adds supporting evidence.
NAVIGATE
Ultrasonic + IMU on a local ESP32 give autonomous obstacle avoidance.
COMMUNICATE
LoRa carries commands and alerts far beyond Wi-Fi range; Wi-Fi carries video.
ASSIST
Fixed supply compartment: water, medicine or a comm device, retrieved by a responder.

## Slide 4
03 AI AT THE CORE
AI proposes. Humans decide. Firmware protects
1
Mission
Operator: "search for people"
2
Capture
ESP32-CAM sends a frame
3
Analyze
Vision AI finds a person + confidence
4
Fuse
Add mmWave + sensor context
5
Confirm
Operator verifies, then acts
Before / after: AI marks a possible person with a confidence score
Vision AI flags possible people from camera frames
mmWave radar is supporting evidence, never proof
Bad or missing AI output never moves the rover
Operator dashboard: live feed, detection box, sensor data

## Slide 5
04 IoT + EMBEDDED SYSTEM
A four-layer IoT stack on low-cost embedded hardware
PERCEPTION
Sensing the world
ESP32-CAM
HC-SR04 ultrasonic
MPU9250 IMU
mmWave radar
DHT11
EDGE (EMBEDDED)
Real-time, offline-capable
Main ESP32
Motor control
Sensor fusion
Safety state machine
E-stop
CONNECTIVITY
Two radios, two jobs
Wi-Fi: video + dashboard
LoRa SX1278: commands, alerts
ACK + timeout
INTELLIGENCE
Advisory, not critical
Gateway
Vision AI API
Mission planning
Incident summary

## Slide 6
05 DUAL COMMUNICATION
Wi-Fi for video. LoRa for survival
Wi-Fi / IP
Live video + JPEG snapshots
Dashboard + low-latency control
Gateway sends frames to AI
Needs an IP path for cloud AI
LoRa
Compact commands + telemetry
Event alerts + node health
Works with no Wi-Fi at all
Too slow for video, built for range
Reliability built in
Message IDs
Sequence numbers
ACK on critical commands
Timeout detection
Safe stop on link loss

## Slide 7
06 EMBEDDED SAFETY
Deterministic onboard rules always win
BOOT / SELF-CHECK
Sensors, radio, motor driver
SAFE STOP
Motors off. Report fault. Wait.
MANUAL
Validated operator commands only
AUTONOMOUS
Local navigation + obstacle checks
SEARCH / ASSIST
Capture, AI advisory, operator confirms
fault / timeout
Any mode to SAFE STOP when:
Physical E-stop pressed
Obstacle threshold crossed
Critical sensor invalid
Command stale / link lost
Motor driver fault
AI output missing or malformed

## Slide 8
07 OPERATION + LIVE DEMO
Three modes, one demo story
MANUAL
Live video, web or LoRa control, real-time telemetry
AUTONOMOUS
Obstacle avoidance, explore area, AI human detection
DISASTER ASSIST
Detect, mark location, deliver supplies, two-way contact
Mock disaster-zone demo flow
1
Drive
Manual run with live video
2
Traverse
Auto stop, scan, turn, re-check
3
Detect
Test image + radar event
4
Alert
LoRa telemetry, Wi-Fi unplugged
5
Hand-off
Stop; responder takes item

## Slide 9
08 BUILD PLAN AND HONEST SCOPE
Reliable core first. AI on top. No overclaiming
01
Motor + E-stop
02
Ultrasonic safety
03
LoRa link
04
Camera + dashboard
05
AI gateway
06
Integrated tests
Demonstrates today
Remote visual inspection
Possible-person image flagging
Obstacle avoidance
LoRa telemetry + alerts
Optional fixed supply box
Not claimed
Seeing through smoke or rubble
Reliable buried-survivor location
Medical diagnosis
Full autonomous mapping
Certified life-safety use
Next upgrades
Thermal camera
Calibrated gas sensors
Wheel encoders + LiDAR SLAM
On-device edge AI (TinyML)
Solar charging

## Slide 10
AURA-X
A practical step toward safer remote disaster inspection
AI-assisted perception + edge-safe navigation
LoRa-connected alerts + human-supervised assistance
"Detect possible signs. Report the evidence. Keep responders in control."
Thank you | Questions?